## Slide 1: Modern BCI: the need for next-generation wireless technologies
Dr. Paul Wanda, PhD
Engineer & Project Manager
Blackrock Microsystems Europe GmbH
B-CRATOS Consortium Partner

## Slide 2: Great need for improved assistive and rehabilitative technologies
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME
Example: Spinal Cord Injury
  At least half a million estimated to be affected in Europe and the US
  Terrible impact on quality of life
  Up to a 4.5M Euro lifetime cost, not including lost wages, benefits, productivity
  Less than 1% experience complete recovery before hospital discharge
Stroke (1.1M/yr EUR), ALS, many other indications
White House File Photo 2016
“Functional/Motor Outcome 5 years after Stroke is equivalent to outcome at 2 months”
(Meyer et al 2015, Stroke)
Notes: ALS: 30k tetraplegia: 177k
PD: 1 million epilepsy: 3.4 million
ED: 30 million

## Slide 3: What will be the impact of BCI?
BCI systems convert recorded brain activity into control signals for external devices, such as computers, prosthetics, vehicles, or even stimulators to restore movement to lost limbs.
Reduce reliance on outside care.
Empower new rehabilitative approaches.
Return to work and increased independence.
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME

## Slide 4: What do prospective users want?
SCI: Collinger et al 2013
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME

## Slide 5: What has been demonstrated?
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME
Fig. Willett et al 2023
Fig. Flesher et al 2021
60+ words/minute speech decoding
5D prosthetic control with tactile feedback
Img. The Guardian, 2005.
BrainGate 2004
Hochberg et al 2006
Device and prosthetic control

## Slide 6: Where are the market-ready BCI systems?
There is a growing number of implantable devices on the market for other indications:
  DBS for Parkinsons, Tremor, related diseases
  RNS to treat Epilepsy
  Peripheral stimulation systems (epilepsy, pain, etc.)
  Cochlear implants
Similar characteristics to an imagined BCI system!
  Fully implantable, electrodes in/near brain tissue, capable of data collection and/or stimulation, on-board logic, wireless powering
These devices have served as a model for many proposed BCI systems but there are critical differences as we will see...
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME

## Slide 7: DBS treatment
DBS systems for Parkinson’s disease typically deliver stimulation to one of four electrode contacts (per hemisphere) and must not record data for the therapy
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME
Implanted to chest, tunnelled wires to skull

## Slide 8: EEG/ECoG data collection for Epilepsy
To diagnose and localize focal epilepsy, clinical EEG systems sample data from hundreds of electrode contacts (usually 1kHz)
256 channels @ 16 bits  4 Mbps
  Wired devices in clinic
  Percutaneous
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME

## Slide 9: Epilepsy Treatment
The Neuropace RNS records from up to 4 pairs of channels, storing small snippets of data (250 Hz). Stimulates multiple channels.
4 channels @ 10 bits  10 kbps
  Fully implantable
  Data stored on device. Most recent 4 minutes can be sent to external device.
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME

## Slide 10: Data collection for BCI Research
BCI research programs typically implant 2 multi-electrode arrays, up to 128 channels per array, sampling ~30 kHz.
  Chen et al 2020/2023 -> 1024 channels w/ 16 arrays
256 channels @ 16 bits  122 Mbps
  Wired devices with percutaneous connectors, large external hardware
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME

## Slide 11: BCI’s big data challenge
Unlike with the other therapies/devices, BCI has demanding needs for data:
  High Number of Channels
  Anatomical Coverage (not just surface but depth)
  High sampling rate and data resolution
  Microelectrodes: redundancy and stability for the long term
On-board processing/multiplexing can mitigate this need, but pose other challenges and sacrifices (ex. power, size)
Raw, high-quality neural data will be long in-demand to support new training models and algorithms, new biomarkers of disease
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME

## Slide 12: Do we need big data for BCI?
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME
BCI control has been demonstrated using data collected at lower sampling rates, such as HF-LFPs (Flint et al 2013, Heldman and Moran 2020)
However, the gold standard remains spiking activity of single neurons in motor cortex (see left).
GPT-4 trained on 10 trillion words!
  Need not only data volume, but also data quality
Fig. Willett et al 2023

## Slide 13: Do we need big data for BCI?
Neuropixels 2.0
Neuralink “Link”
Blackrock “Neuralace”
96 electrode “threads” with 32 electrodes per thread (2019)
1280 recording sites per shank
5120 per device
10000+ channels
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME
The electrode market is looking towards ever increasing channel counts for future BCI
and Axoft!
Ultrasoft HD electrodes

## Slide 14: The need for WIRELESS solutions
Wires through the skin
  Infection risk
  Damage to device
  Additional surgeries
Wires in the body
  Same as above
  Scar tissue formation (“bowstringing”)
  Managing large numbers of channels/wires
Aesthetics, Everyday Use
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME

## Slide 15: Where does current wireless tech stack up?
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME
Technology | Typical Data Rates | Compared to Basic Research BCI Need (~100 Mbps)
Zigbee | 250 kbps | 0.2%
MedRadio | 400 kbps (theor. higher) | 0.3%
NFC/RFID | 850 kbps | 0.7%
Bluetooth Low Energy (BLE) | < 1 Mbps (theor. ~2.1 Mbps) | 0.8%
Ultrawideband (UWB) | 10s of Mbps (theor. higher) | 8+%
Optical (var) | 10s of Mbps | 8+%

## Slide 16: Where does current wireless tech stack up?
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME
Technology | Typical Data Rates | Compared to Basic Research BCI Need (~100 Mbps)
Zigbee | 250 kbps | 0.2%
MedRadio | 400 kbps (theor. higher) | 0.3%
NFC/RFID | 850 kbps | 0.7%
Bluetooth Low Energy (BLE) | < 1 Mbps (theor. ~2.1 Mbps) | 0.8%
Ultrawideband (UWB) | 10s of Mbps (theor. higher) | 8+%
Optical (var) | 10s of Mbps | 8+%
B-CRATOS (RFBS, Fat-IBC) | 10s to 100s of Mbps | Target: 100%

## Slide 17: A growing BCI landscape
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME

## Slide 18: B-CRATOS: a vision of everyday BCI
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME
B-CRATOS is pioneering a wireless implantable neural bypass platform designed to support big data applications.
Fat IBC Bidirectional In-Body Data
Wireless Implants
Direct Brain Stimulation Feedback
- Very low energy wireless data transmission (< 50 mW)
- State of the art neural ASIC
- No implanted wires
- No implanted batteries
- Bidirectional data flow
- Micro-stimulation
- Big Neural Data Readout
- Sensorised prosthetic hand
Please attend to BCRATOS Team:
Dr. Augustine, Dr. Scherberger, Dr. Controzzi, and Dr. Khaleghi’s talks later in the workshop for more technical details!

## Slide 19: B-CRATOS Integrated System
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME
We will demonstrate on the bench and animal demonstrator:
  Low latency wireless readout and stimulation feedback from microelectrodes via backscatter and Fat-IBC channel (< 100 ms, first target: 32 Mbps)
  Battery-less implant electronics
  Data supports rapid decoding for hand prosthetic control
in vivo demonstrator in NHP (Scherberger Lab, DPZ)
Next generation (BCRATOS 2.0): refined prototype to support future pre-clinical and clinical trials (by 2029)

## Slide 20
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME

## Slide 21: The B-CRATOS project has received funding from the European Union’s Horizon 2020 research and innovation programme under GA No 965044
Wireless Brain-Connect inteRfAce TO machineS
b-cratos.eu
please send comments to pwanda@blackrockneuro.com
Enabling Independence through Next-Generation Brain-Machine-Body Connectivity
Neural Horizons Workshop, Gardanne, France – 19-02-2025
Dr. Paul Wanda, PhD - BRME